Advanced Ocean Color Scanner

© 2010     M. T. Smirnov1, Yu. G. Tishchenko1*, Yu. M. Gektin2,

N. P. Akimov2, A. M. Solov’ev2, O. V. Kopelevich3

1 Institute of Radioengineering and Electronics, Russian Academy of Sciences,

Fryazino, Moscow Region

2 Federal State Unitary Enterprise “Russian Institute of Space Device Engineering”, Moscow

3 P.P. Shirshov Institute of Oceanology, Russian Academy of Sciences, Moscow

* E-mail: tishchen@ire.rssi.ru

A new satellite instrument (Advanced Ocean Color Scanner) is designed for studies of ocean environment and of main climatic factors. It is intended for biological and ecological monitoring of seas and oceans as well as for investigations of physical processes in their upper layer. A peculiarity of the new scanner is that provides data not only from measurements in different spectral ranges but also from along-track scanning in three spectral bands. That gives additional information for better atmospheric correction.

Key words: multi-spectral scanning system, space experiment, ocean color, biological and biochemical characteristics, ecological monitoring.

Table  Main performance characteristics of the advanced ocean color scanner ROSS-1

.

| Parameters | Values |
| --- | --- |
| Spectral bands* , ( (8 bands at across track scanning) | 0.402-0.422 0.433-0.453 0.480-0.500 0.500-0.520 0.545-0.565 0.660-0.680 0.725-0.765 0.845-0.885 |
| Uncertainty in the edge of spectral band, nm | (5 |
| Viewing angle, degrees | 66 ((33) |
| Swath, km | >900 |
| Angular resolution, mrad | 0.65(0.05 |
| Spatial resolution at nadir (with the orbit altitude of 800 km), km | 0.5(0.1 |
| Operating mode | by sessions |
| Duration of continuous work, min | (30 |
| Interval between the sessions, min | (20 |
| Power consumption | <100 W |
| Weight, kg | <40 |

*At least three spectral bands are planned for the along-track scanning (their parameters will be defined

during the engineering process)